## Slide 1: Scratch Detection

## Slide 2
Filter Wafers
Filter by Wafer size, by three ranges conditions:
Less than 35: No scratches
35<->63:
  Line: -0.001*wafer_size+0.19:
  If above the line no scratches.
  If below the line, there is scratches.
63<->infinity
  Line:-0.0003* wafer_size+0.13
  If above the line no scratches.
  If below the line, there is scratches.

## Slide 3
Filter Wafers
Train Wafers number: 3920
Flow:
Wafers number: 2372
Wafers selected: 1000
Hyper-parameters search
Two parameters:
Polynomial order: Order of the polynomial fit to the scratch
The ink pixels strength weight: penalized on the model score for including good dies.
Three values considered for each: total of 9 combination tested
The model (described later) was
applied to each combination
Scratch prediction
Predictions on the test set:
Filter by Wafers size
With the best parameters (F1 score=48%) from last the Hyper-parameter search (Polynomial order=3. Ink pixels strength weight =-0.5)
Train
Test

## Slide 4
Wafer: 97a213
Model for scratch detection:

## Slide 5
Bad Dies
Segments with area >= 3
CC #1
2
4
3
Connected
Components
Connected Components of Bad Dies
and filter out segment below given threshold (=3)

## Slide 6
All possible combinations
1
2
4
3
No. | Score
1 | 0.040
2 | 4.049
3 | 6.046
4 | 5.681
5 | 4.037
6 | 6.966
7 | 0.180
8 | 11.903
9 | 10.407
10 | 11.041
11 | 8.600
12 | 2.704
13 | 4.3906
14 | 15.882
15 | 3.5259
[1] [2] [3] [4]
[1 2] [1 3] [1 4] [2 3]
[2 4] [3 4] [1 2 3] [1 2 4]
[1 3 4] [2 3 4] [1 2 3 4]
Best
score

## Slide 7
Original points
Centralized to (0,0)
Rotated to horizontal
orientation
Polynomial fit (order 3)
Combination #14
Fitting the points
(no_points = 14)

## Slide 8
Original points
Centralized to (0,0)
Rotated to horizontal
orientation
Polynomial fit (order 3)
Fitting the points
Combination #15
(no_points = 17)

## Slide 9
Score Calculation
Zoom
Combination #14
Fit_score = e0.1 [ (# bad_dies) – 0.5*(# good_dies) ]
= e0.1 [14 – 0.5*12] = e0.8
= 2.2255
L
W
Slend_ratio = W / L = 4.17 / 17 = 0.245
Slender_score = min(-2*Slend_ratio + 1, 0.01)
= 0.5098
Final_score = Fit_score * Slender_score * no_points = 2.2255 * 0.5098 * 14 = 15.88
1
Slend_ratio
Slend_score
0.5
0.01

## Slide 10
Score Calculation
Zoom
Combination #15
Fit_score = e0.1 [ (# bad_dies) – 0.5*(# good_dies) ]
= e0.1 [10 – 0.5*25] = e-2.5
= 0.7788
Slend_ratio = W / L = 8.547 / 23.3 = 0.3668
Slender_score = min(-2*Slend_ratio + 1, 0.01)
= 0.2664
Final_score = Fit_score * Slender_score * no_points = 0.7788 * 0.2664 * 17 = 3.53
L
W
Ink pixels strength weight = -0.5

## Slide 11
Combination #14 gives the best score
Final Detection